## Slide 1: 32-bit Carry Look-Ahead Adder
Team DK
Darius San Agustin & Kevin Chen
EE 457 – Digital Integrated Circuits – Prof. Bruce Kim

## Slide 2: Background & Introduction

## Slide 3: Background & Introduction
Performs binary addition, just like the ripple-carry adder
Carry-Look Ahead adder computes all carry-in signals for all full adders in near-constant time
  As opposed to the RCA which has a time complexity of O(n)

## Slide 4: Background & Introduction
Use gates & modules designed in previous projects
  Two-input NAND
  CMOS Inverter
  Two-input XOR
  Full Adder

## Slide 5: NAND

## Slide 6: Inverter (with wells)

## Slide 7: Inverter (No Wells)

## Slide 8: XOR

## Slide 9: XOR

## Slide 10: Background & Introduction
Modified Full Adder
  Removed carry-out output
  Added outputs for propagate P and generate G

## Slide 11: Background & Introduction
LCU Modules – C1, C2, C3
  Computes carry-in signal for second, third, and fourth full adder, respectively

## Slide 12: Background & Introduction
Extra modules for scalability
    This takes the same form as C3, so no need to design a new component!

## Slide 13: Background & Information
With four full adders and all these LCU modules, we can design a four-bit CLA adder that’s scalable, i.e. usable in higher designs
We then use the four-bit CLA adders and the same LCU modules to build a 16-bit CLA
We scale up again, using the 16-bit CLAs to build the final circuit: the 32-bit CLA

## Slide 14: Electric Schematic

## Slide 15: Modified Full Adder

## Slide 16: C1 Module

## Slide 17: C2 Module

## Slide 18: C3 Module

## Slide 19: PG4 Module

## Slide 20: 4-bit Fast Adder

## Slide 21: 16-bit Fast Adder

## Slide 22: 32-bit Fast Adder

## Slide 23: 32-bit Fast Adder (No boxes!)
Screenshots are separate due to rendering issues with Electric
This is an overview

## Slide 24: Electric Layout

## Slide 25: Modified Full Adder

## Slide 26: C1 Module

## Slide 27: C2 Module

## Slide 28: C3 Module
NAND and Inverter layouts used here are slightly taller than in the C1 and C2 modules
  Also in the PG4 module, next slide

## Slide 29: PG4 Module

## Slide 30: 4-bit Fast Adder

## Slide 31: 16-bit Fast Adder

## Slide 32: 32-bit Fast Adder (Overview)

## Slide 33: 32-bit Fast Adder (top)

## Slide 34: 32-bit Fast Adder (bottom)

## Slide 35: IRSIM Logic Simulations

## Slide 36: Additions
Total of Five Additions
 | Input: A (Hexadecimal) | Input: B (Hexadecimal) | Expected Output: S (Hexadecimal)
First Addition | 0x7FFFFFFF | 0x00000001 | 0x80000000
Second Addition | 0x7FFFFFFF | 0x80000000 | 0xFFFFFFFF
Third Addition | 0x12162019 | 0x00040000 | 0x121A2019
Fourth Addition | 0x11031997 | 0x01130682 | 0x12162019
Fifth Addition | 0x09161998 | 0x09000681 | 0x12162019

## Slide 37: Additions
Total of Five Additions
 | Input: A (Decimal) | Input: B (Decimal) | Expected Output: S (Decimal)
First Addition | 2147483647 | 1 | 2147483648
Second Addition | 2147483647 | 2147483648 | 4294967295
Third Addition | 303439897 | 262144 | 303702041
Fourth Addition | 285415831 | 18024066 | 303439897
Fifth Addition | 152443288 | 150996609 | 303439897

## Slide 38: Waveforms – Input A(0:15)

## Slide 39: Waveforms – Input A(16:31)

## Slide 40: Waveforms – Input B(0:15)

## Slide 41: Waveforms – Input B(16:31)

## Slide 42: Waveforms – Output S(0:15)

## Slide 43: Waveforms – Output S(16:31)

## Slide 44: Subtractions
Total of Five Subtractions
 | Input: A (Hexadecimal) | Input: B (Hexadecimal) | Expected Output: S (Hexadecimal)
First Subtraction | 0x80000000 | -0x00000001 = 0xFFFFFFFF | 0x7FFFFFFF
Second Subtraction | 0xFFFFFFFF | -0x80000000 = 0x80000000 | 0x7FFFFFFF
Third Subtraction | 0x121A2019 | -0x00040000 = 0xFFFC0000 | 0x12162019
Fourth Subtraction | 0x12162019 | -0x01130682 = 0xFEECF97E | 0x11031997
Fifth Subtraction | 0x12162019 | -0x09000681 = 0xF6FFF97F | 0x09161998

## Slide 45: Subtractions
Total of Five Subtractions
 | Input: A (Decimal) | Input: B (Decimal) | Expected Output: S (Decimal)
First Subtraction | 2147483648 | -1 | 2147483647
Second Subtraction | 4294967295 | -2147483648 | 2147483647
Third Subtraction | 303702041 | -262144 | 303439897
Fourth Subtraction | 303439897 | -18024066 | 285415831
Fifth Subtraction | 303439897 | -150996609 | 152443288

## Slide 46: Waveforms – Input A(0:15)

## Slide 47: Waveforms – Input A(16:31)

## Slide 48: Waveforms – Input B(0:15)

## Slide 49: Waveforms – Input B(16:31)

## Slide 50: Waveforms – Output S(0:15)

## Slide 51: Waveforms – Output S(16:31)

## Slide 52: Logic Simulations
It all checks out.
 | Expected Output (Hexadecimal) | Output Schematic (Hexadecimal) | Output Layout (Hexadecimal)
First Addition | 0x80000000 | 0x80000000 | 0x80000000
Second Addition | 0xFFFFFFFF | 0xFFFFFFFF | 0xFFFFFFFF
Third Addition | 0x121A2019 | 0x121A2019 | 0x121A2019
Fourth Addition | 0x12162019 | 0x12162019 | 0x12162019
Fifth Addition | 0x12162019 | 0x12162019 | 0x12162019
First Subtraction | 0x7FFFFFFF | 0x7FFFFFFF | 0x7FFFFFFF
Second Subtraction | 0x7FFFFFFF | 0x7FFFFFFF | 0x7FFFFFFF
Third Subtraction | 0x12162019 | 0x12162019 | 0x12162019
Fourth Subtraction | 0x11031997 | 0x11031997 | 0x11031997
Fifth Subtraction | 0x09161998 | 0x09161998 | 0x09161998

## Slide 53: Logic Simulations
It all checks out.
 | Expected Output (Decimal) | Output Schematic (Decimal) | Output Layout (Decimal)
First Addition | 2147483648 | 2147483648 | 2147483648
Second Addition | 4294967295 | 4294967295 | 4294967295
Third Addition | 303702041 | 303702041 | 303702041
Fourth Addition | 303439897 | 303439897 | 303439897
Fifth Addition | 303439897 | 303439897 | 303439897
First Subtraction | 2147483647 | 2147483647 | 2147483647
Second Subtraction | 2147483647 | 2147483647 | 2147483647
Third Subtraction | 303439897 | 303439897 | 303439897
Fourth Subtraction | 285415831 | 285415831 | 285415831
Fifth Subtraction | 152443288 | 152443288 | 152443288

## Slide 54: LTSPICE Code and Parasitic Extractions

## Slide 55: SPICE Code
vdd vdd 0 DC 3.3 vgnd gnd 0 DC 0 va0 a0 0 PULSE(3.3 0 250n 100p 100p 500n 1000n) va1 a1 0 PULSE(3.3 0 250n 100p 100p 500n 1000n) ... va31 a31 0 PULSE(3.3 0 250n 100p 100p 500n 1000n) vb0 b0 0 DC 0 vb1 b1 0 DC 0 ... vb31 b31 0 DC 0 .meas TRAN tr0 TRIG V(s0) VAL=.33 RISE=1 TARG V(s0) VAL=2.97 RISE=1 .meas TRAN tr1 TRIG V(s1) VAL=.33 RISE=1 TARG V(s1) VAL=2.97 RISE=1 ... .meas TRAN tr31 TRIG V(s31) VAL=.33 RISE=1 TARG V(s31) VAL=2.97 RISE=1

## Slide 56: SPICE Code
.meas TRAN tf0 TRIG V(s0) VAL=2.97 FALL=1 TARG V(s0) VAL=.33 FALL=1 .meas TRAN tf1 TRIG V(s1) VAL=2.97 FALL=1 TARG V(s1) VAL=.33 FALL=1 ... .meas TRAN tf31 TRIG V(s31) VAL=2.97 FALL=1 TARG V(s31) VAL=.33 FALL=1 .meas TRAN tplh0 TRIG V(a0) VAL=1.65 RISE=1 TARG V(s0) VAL=1.65 RISE=1 .meas TRAN tplh1 TRIG V(a1) VAL=1.65 RISE=1 TARG V(s1) VAL=1.65 RISE=1 ... .meas TRAN tplh31 TRIG V(a31) VAL=1.65 RISE=1 TARG V(s31) VAL=1.65 RISE=1 .meas TRAN tphl0 TRIG V(a0) VAL=1.65 FALL=1 TARG V(s0) VAL=1.65 FALL=1 .meas TRAN tphl1 TRIG V(a1) VAL=1.65 FALL=1 TARG V(s1) VAL=1.65 FALL=1 ... .meas TRAN tphl31 TRIG V(a31) VAL=1.65 FALL=1 TARG V(s31) VAL=1.65 FALL=1 .tran 1000n .include C:\Electric\kim_models.txt

## Slide 57: Parasitic Extractions
Output | Capacitance
s0 | 6.129fF
s1 | 6.129fF
s2 | 6.37fF
s3 | 6.37fF
s4 | 6.37fF
s5 | 6.37fF
s6 | 6.37fF
s7 | 6.37fF
s8 | 6.37fF
s9 | 6.37fF
s10 | 6.37fF
s11 | 6.37fF
s12 | 6.37fF
s13 | 6.37fF
s14 | 6.37fF
s15 | 6.37fF
s16 | 7.288fF
s17 | 6.129fF
s18 | 6.129fF
s19 | 6.129fF
s20 | 6.129fF
s21 | 6.129fF
s22 | 6.129fF
s23 | 6.129fF
s24 | 6.129fF
s25 | 6.129fF
s26 | 6.129fF
s27 | 6.129fF
s28 | 6.129fF
s29 | 6.129fF
s30 | 6.129fF
s31 | 6.129fF

## Slide 58: Parasitic Extractions
Component | RP (Ω) | RN (Ω)
Inverter (Tall) | 8.138 | 7.75
Inverter | 9.455 | 8.525
Inverter (no wells) | 9.455 | 8.525
NAND (A input) | 9.854 | 7.75
NAND (B input) | 9.688 | 9.817
NAND (Tall version, A input) | 9.3 | 9.61
NAND (Tall version, B input) | 6.2 | 9.106
XOR | 9.079 | 9.079
PG4 | 8.82975 | 6.717

## Slide 59: Measurements in LTSPICE
Rise Time, Fall Time, and Propagation Delay for both Schematic and Layout

## Slide 60: Waveforms – Input A

## Slide 61: Waveforms – Input A

## Slide 62: Waveforms – Input B

## Slide 63: Waveforms – Input B

## Slide 64: Schematic - Output S

## Slide 65: Schematic - Output S
Also verifies -1 + 0 = -1
0xFFFFFFFF + 0x00000000 = 0xFFFFFFFF

## Slide 66: Schematic Metrics
Bit | Rise Time (ps) | Fall Time (ps) | tplh (ps) | tphl (ps) | tp (ps)
0 | 99.08 | 97.81 | 467.63 | 427.63 | 447.6255
1 | 103.41 | 101.43 | 481.84 | 438.37 | 460.1045
2 | 99.76 | 101.11 | 437.52 | 403.74 | 420.634
3 | 101.63 | 98.98 | 393.08 | 367.27 | 380.1725
4 | 98.07 | 100.29 | 467.68 | 426.55 | 447.116
5 | 103.42 | 101.45 | 481.84 | 438.38 | 460.1085
6 | 99.76 | 101.11 | 437.52 | 403.75 | 420.6385
7 | 101.63 | 98.98 | 393.08 | 367.27 | 380.177
8 | 98.07 | 100.29 | 467.68 | 426.51 | 447.0975
9 | 103.42 | 101.42 | 481.84 | 438.35 | 460.0955
10 | 99.76 | 101.12 | 437.52 | 403.73 | 420.6265
11 | 101.63 | 98.98 | 393.08 | 367.26 | 380.1695
12 | 98.07 | 100.21 | 467.68 | 426.48 | 447.081
13 | 103.42 | 101.41 | 481.84 | 438.32 | 460.081
14 | 99.76 | 101.11 | 437.52 | 403.69 | 420.605
15 | 101.63 | 98.97 | 393.08 | 367.24 | 380.1585

## Slide 67: Schematic Metrics
Bit | Rise Time (ps) | Fall Time (ps) | Tplh (ps) | Tphl (ps) | Tp (ps)
16 | 97.61 | 99.92 | 467.58 | 426.89 | 447.233
17 | 103.42 | 101.45 | 481.84 | 438.37 | 460.105
18 | 99.76 | 101.11 | 437.52 | 403.74 | 420.634
19 | 101.63 | 98.98 | 393.08 | 367.27 | 380.1725
20 | 98.08 | 100.29 | 467.69 | 426.55 | 447.1165
21 | 103.42 | 101.45 | 481.84 | 438.38 | 460.109
22 | 99.76 | 101.11 | 437.52 | 403.75 | 420.6385
23 | 101.63 | 98.98 | 393.08 | 367.27 | 380.177
24 | 98.07 | 100.29 | 467.68 | 426.51 | 447.0975
25 | 103.42 | 101.42 | 481.84 | 438.35 | 460.0955
26 | 99.76 | 101.12 | 437.52 | 403.73 | 420.6265
27 | 101.63 | 98.98 | 393.08 | 367.26 | 380.17
28 | 98.07 | 100.21 | 467.68 | 426.48 | 447.081
29 | 103.42 | 101.41 | 481.84 | 438.32 | 460.081
30 | 99.76 | 101.11 | 437.52 | 403.69 | 420.605
31 | 101.63 | 98.98 | 393.08 | 367.24 | 380.159
Average Rise Time
  100.74 ps
Average Fall Time
  100.36 ps
Average Prop. Delay
  427.0185 ps

## Slide 68: Layout - Output S

## Slide 69: Layout - Output S

## Slide 70: Layout Metrics
Bit | Rise Time (ns) | Fall Time (ns) | tplh (ns) | tphl (ns) | tp (ns)
0 | 1.6947 | 1.0267 | 2.1432 | 1.6739 | 1.908515
1 | 1.7027 | 1.0296 | 2.2131 | 1.7266 | 1.969865
2 | 1.7836 | 1.0709 | 2.2570 | 1.7569 | 2.00693
3 | 1.8039 | 1.0846 | 2.1466 | 1.6678 | 1.90721
4 | 1.7148 | 1.0365 | 2.1549 | 1.6780 | 1.916425
5 | 1.7102 | 1.0329 | 2.2162 | 1.7285 | 1.97233
6 | 1.7861 | 1.0728 | 2.2582 | 1.7576 | 2.007895
7 | 1.8048 | 1.0850 | 2.1470 | 1.6680 | 1.90749
8 | 1.7176 | 1.0382 | 2.1561 | 1.6788 | 1.91745
9 | 1.7131 | 1.0342 | 2.2174 | 1.7292 | 1.97327
10 | 1.7894 | 1.0753 | 2.2599 | 1.7585 | 2.00918
11 | 1.8086 | 1.0868 | 2.1486 | 1.6689 | 1.908745
12 | 1.7210 | 1.0401 | 2.1576 | 1.6797 | 1.918685
13 | 1.7411 | 1.0466 | 2.2293 | 1.7364 | 1.98281
14 | 1.7919 | 1.0772 | 2.2611 | 1.7592 | 2.01013
15 | 1.8096 | 1.0873 | 2.1490 | 1.6692 | 1.909095

## Slide 71: Layout Metrics
Average Rise Time
  1.7540 ns
Average Fall Time
  1.0568 ns
Average Prop. Delay
  1.951 ns
Bit | Rise Time (ns) | Fall Time (ns) | Tplh (ns) | Tphl (ns) | Tp (ns)
16 | 1.7274 | 1.0442 | 2.1601 | 1.6819 | 1.92098
17 | 1.7027 | 1.0296 | 2.2131 | 1.7266 | 1.969865
18 | 1.7776 | 1.0663 | 2.2541 | 1.7552 | 2.00463
19 | 1.7970 | 1.0813 | 2.1437 | 1.6661 | 1.904915
20 | 1.7088 | 1.0330 | 2.1520 | 1.6763 | 1.914135
21 | 1.7033 | 1.0299 | 2.2134 | 1.7268 | 1.97009
22 | 1.7801 | 1.0682 | 2.2553 | 1.7559 | 2.0056
23 | 1.7979 | 1.0817 | 2.1441 | 1.6663 | 1.905195
24 | 1.7116 | 1.0346 | 2.1533 | 1.6771 | 1.91517
25 | 1.7063 | 1.0312 | 2.2146 | 1.7275 | 1.971025
26 | 1.7835 | 1.0708 | 2.2570 | 1.7568 | 2.006885
27 | 1.8017 | 1.0835 | 2.1457 | 1.6672 | 1.90645
28 | 1.7150 | 1.0366 | 2.1548 | 1.6780 | 1.916405
29 | 1.7346 | 1.0437 | 2.2263 | 1.7347 | 1.980475
30 | 1.7860 | 1.0727 | 2.2582 | 1.7575 | 2.007835
31 | 1.8028 | 1.0841 | 2.1461 | 1.6675 | 1.9068

## Slide 72: Comparison
The parasitic effects drastically slow the performance of the CLA
Compared to schematic results, the layout:
  Avg. Rise time is 17.41 times slower
  Avg. Fall Time is 10.53 times slower
  Avg. Prop. Delay is 4.57 times slower

## Slide 73: Other Measurements in LTSPICE
Steady-State Power Dissipation, Total Chip Area, Total Transistor Count

## Slide 74: Power
I(VDD)
P = VDD * I(VDD)
P = 3.3 V * 286.828 µA
P = 946.5324 µW

## Slide 75: Total Chip Area
A = dX * dY
A = 1400λ * 2886λ
A = 4,040,400*λ^2
A = 4,040,400 * (.175 µm)^2
A = 123,737.25 sq. µm

## Slide 76: Total Transistor Count
Transistor count of Gates
Transistor count of LCU Modules

## Slide 77: Total Transistor Count
4-bit CLA
16-bit CLA

## Slide 78: Total Transistor Count
32-bit Fast Adder (Final Product)

## Slide 79: Conclusion
We made it!

## Slide 80: Conclusion
Can perform addition and subtraction (by inputting two’s complement of a binary number)
It’s bigger and bulkier than the Ripple Carry Adder
  But it’s faster!
Space-Time Tradeoff
  We use more space and design more complex logic circuits
  In return, we get faster performance when performing binary addition/subtraction operations